## Slide 1: Representation of Numbers
Fixed Point Representation,
Addition and subtraction of signed 2’s complement numbers
Members: Kyrshanlang R Dkhar, Almora R Kharkamni, Jordan R Kharkrang and K Lalhriatpuia
Roll no: 1,10,18,30

## Slide 2: Contents
  Introduction
  Fixed Point Representation
  Addition of signed 2’s complement numbers
  Subtraction of signed 2’s complement numbers

## Slide 3: Representation of Numbers
  Number Systems
  Decimal Number System (0-9)
  Binary Number System (0 and 1)
  Octal Number System (0-7)
  Hexadecimal Number System (0-9,A-F)

## Slide 4: Binary-Coded Octal Numbers
OCTAL NUMBER | Binary-coded Octal | Decimal equivalent
0 | 000 | 0
1 | 001 | 1
2 | 010 | 2
3 | 011 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
10 | 001 000 | 8
11 | 001 001 | 9
24 | 010 100 | 20

## Slide 5: Binary-Coded Hexadecimal Numbers
HEXADECIMAL NUMBER | Binary-coded Hexadecimal | Decimal equivalent
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
A | 1010 | 10
32 | 0011 0010 | 50
F8 | 1111 1000 | 248

## Slide 6: Decimal Representation: BCD
  BCD Binary Coded Decimal
    Uses 4-bit to represent decimal numbers (0-9)
DECIMAL NUMBER | BCD NUMBER
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1000
10 | 0001 0000
20 51 | 0010 0000 0101 0001

## Slide 7: Fixed-Point Representation
  How are fractions represented in Registers?
    E.g: (0100.1010)
  Binary point (.)
  Two ways to specify the position of the binary point.
    Fixed-point representation
    Floating-point representation (Group 6)

## Slide 8: Fixed-Point Representation
  Fixed-point
    Binary point is assumed to be fixed in one position:
        Extreme left of Register
        Binary Number is interpreted as a Fraction binary number
            .0100101
        Extreme Right of Register
        Binary Number is interpreted as an Integer binary number
            0100101.

## Slide 9: Integer Representation : Binary Numbers
  Signed and Unsigned Binary Numbers
  For 8-bit Register the Range is
    Signed (-128 to +127) i.e. (10000000 to 01111111)
    Unsigned (0 to 255) i.e. (00000000 to 11111111)
  Signed Binary Number : Positive Number
    Sign bit : 0 (leftmost bit)
    Magnitude: is the binary number
    E.g: +6 is represented as 00000110 in 8-bit register

## Slide 10: Integer Representation : Binary Numbers
  Signed Binary Number : Negative Number
    Sign bit : 1 (leftmost bit)
    Magnitude: binary number can be represented in three ways
      Signed-magnitude representation
        -6 is represented as 10000110
      Signed-1’s complement representation
        -6 is represented as 11111001
      Signed-2’s complement representation
        -6 is represented as 11111010

## Slide 11: Addition of Signed-2’s complement numbers
  Procedure for Addition:
    Add the Two Numbers (include sign bit).
    If there is an end carry discard it.
    The result of addition is the sum of the numbers.
    Negative Binary Numbers are in their signed-2’s complement form before they are added.
    If the sum is negative, then it is in 2's complement.

## Slide 12: Addition of Signed-2’s complement numbers
  E.g: Addition
    6 + 3 2. 6 + (-3)
    +6 00000110 +6 00000110
    +3 00000011 -3 11111101
    = +9 00001001 = +3 00000011
    More E.g:
    -6 + (-3)
    -6 + 3
    6 + 13

## Slide 13: Addition of Signed-2’s complement numbers
  Overflow
    Occurs when sum of two n digits result in an n+1 digits number.
    E.g
    carries: 0 1 carries: 1 0
        (a) +70 0 1000110 (b) -70 1 0111010
        +80 0 1010000 -80 1 0110000
        +150 1 0010110 -150 0 1101010

## Slide 14: Subtraction of Signed-2’s complement numbers
  Procedure for Subtraction:
    Take the 2’s Complement of the Subtrahend and add it with the minuend (include sign bit)
    If there is a carry discard it.
    The result of addition is the difference of the two numbers.

## Slide 15: Subtraction of Signed-2’s complement numbers
  E.g: Subtraction
    6 - 3
    2’s Complement of 3(00000011) is (11111100+1)=11111101
    +6 00000110
    -3 11111101
    = +3 100000011
        Discard the end carry we get 00000011 which is +3 in decimal.

## Slide 16: Subtraction of Signed-2’s complement numbers
    2. 6 - (-3)
    2’s Complement of -3(11111101) is (00000010+1)=00000011
    +6 00000110
    +3 00000011
    = +9 00001001
    More E.g:
    -6 - (-3)
    3 - 3
    -6 - 3

## Slide 17: Bibliography
Book:
  Computer System Architecture 3RD EDITION by M. Morris Mano.
    Pages 85-99.

## Slide 18: THANK YOU